09/09/92
xt link is like laplink or other cable transfer utils
-----------------------

    XTreeLink Users

	
    These notes are intended to clarify misunderstandings regarding 
    cables supported by XTreeLink.  


    Page 4 of the XTreeLink User's Guide states that LapLink(tm), 
    Brooklyn Bridge(tm) or FastLynx(tm) cables can be used with 
    XTreeLink.  The statement should be corrected to state that 
    parallel cables from the above manufacturers are supported by 
    XTreeLink.  Following is a discussion regarding serial cables.


    The chart below shows the pinout of the type of cable used by 
    the XTreeLink when connecting two machines in the Serial I/O 
    RS232 mode. The described cable pinout is a match with the 
    Laplink Pro serial cable.  The RUPP FastLynx red serial cable 
    also matches this specification. Note that Brooklyn Bridge  
    serial cables are different and will not work with XTreeLink.  
    The chart below shows the pinout such that the cable could be 
    built as a 9 pin to 9 pin, 25 pin to 25 pin, or a 9 pin to a 25 
    pin cable. Note that the RUPP cable is built such that it is 
    equipped with both 9 pin and 25 pin connectors on each end.



                      XTreeLink SERIAL I/O CABLE
  
      DA9  DB25                                   DB25   DA9
      pin   pin  sig   port    dir   port    sig   pin   pin
      ------------------------------------------------------
      nc  |  1 | GND |       | <-> |       | GND |  1 |  nc
       3  |  2 | TXD |       | --> |       | RXD |  3 |   2
       2  |  3 | RXD |       | <-- |       | TXD |  2 |   3
       7  |  4 | RTS | 3FC.1 | --> | 3FE.4 | CTS |  5 |   8
       8  |  5 | CTS | 3FE.4 | <-- | 3FC.1 | RTS |  4 |   7
       6  |  6 | DSR | 3FC.5 | <-- | 3FC.0 | DTR | 20 |   4
       5  |  7 | GND |       | <-> |       | GND |  7 |   5
       4  | 20 | DTR | 3FC.0 | --> | 3FC.5 | DSR |  6 |   6




    It is possible to purchase a ready made cable or adapter at a 
    local electronics store or computer supply shop that will work 
    with XTreeLink in the serial I/O mode to avoid having to make 
    your own cable.  The cable type is referred to as a "FULL 
    HANDSHAKE NULL MODEM".  These are usually only available with 
    the DB25 type connectors.  The chart below shows the wiring in a 
    FULL HANDSHAKE NULL MODEM CABLE.  By comparing this cable with 
    the DB25 pinout columns it can be seen that this cable would 
    work with XTreeLink.


                  FULL HANDSHAKE NULL MODEM

            DB25                             DB25
             pin       sig    dir     sig     pin
           ---------------------------------------
              1    |   GND  | <-> |   GND  |   1
              2    |   TXD  | --> |   RXD  |   3
              3    |   RXD  | <-- |   TXD  |   2
              4    |   RTS  | --> |   CTS  |   5
              5    |   CTS  | <-- |   RTS  |   4
              6    |   DSR  | <-- | CD/DTR | 8 & 20
              7    |   GND  | <-> |   GND  |   7
            8 & 20 | CD/DTR | --> |   DSR  |   6


    The FULL HANDSHAKE NULL MODEM can be purchased as a cable 
    assembly that is typically 6 feet long.  Make sure that both 
    ends of the cable are female type DB25 connectors so that the 
    cable can directly connect to the computers serial port 
    connector.  If one end of the cable is the male type it is 
    possible to also purchase a GENDER CHANGER that will convert the 
    male end of the cable to a a female connection. 

    If the cable is not available it is also possible to buy a small 
    1.5 to 3 inch long device called a FULL HANDSHAKE NULL MODEM 
    ADAPTER. This is a small plastic or metal device with the above 
    shown wiring inside that is meant to be used in conjunction with 
    a normal DB25 extension cable.  The extension cable should be a 
    straight through wired cable with all pins connected. 



    Other types of NULL modem cables and adapters are made and sold 
    at the electronics outlets.  In general these other types will 
    NOT work with XTreeLink.  These other types have names similar 
    to "NO HANDSHAKE NULL MODEM", "ASYNCHRONOUS MODEM ELIMINATOR", 
    "STANDARD NULL MODEM", "PRINTER HANDSHAKE ADAPTER", or "THREE 
    WIRE NULL MODEM".  The wiring for several of these types is 
    shown in the tables below.  Please note these are examples and 
    there may be many other types of adapters.  So be careful to 
    purchase only the proper type of cable and or adapter to work 
    with XTreeLink.


                    STANDARD NULL MODEM

           DB25                             DB25
            pin       sig    dir     sig     pin
          ---------------------------------------
             1    |   GND  | <-> |   GND  |   1
             2    |   TXD  | --> |   RXD  |   3
             3    |   RXD  | <-- |   TXD  |   8
           4 & 5  | RTS/CTS| --> |    CD  |   5
             8    |    CD  | <-- | RTS/CTS| 4 & 5
             6    |   DSR  | <-- |   DTR  |  20    
             7    |   GND  | <-> |   GND  |   7
            20    |   DTR  | --> |   DSR  |   6


                  NO HANDSHAKE NULL MODEM

           DB25                             DB25
            pin       sig    dir     sig     pin
          ---------------------------------------
             1    |   GND  | <-> |   GND  |   1
             2    |   TXD  | --> |   RXD  |   3
             3    |   RXD  | <-- |   TXD  |   2
           4 &  5 | RTS/CTS|     |        |  nc
            nc    |        |     | RTS/CTS| 4 &  5
             6    |   DSR  | <-- | CD/DTR | 8 & 20 
             7    |   GND  | <-> |   GND  |   7
           8 & 20 | CD/DTR | --> |   DSR  |   6


                   THREE WIRE NULL MODEM

           DB25                             DB25
            pin       sig    dir     sig     pin
          ---------------------------------------
             2    |   TXD  | --> |   RXD  |   3
             3    |   RXD  | <-- |   TXD  |   2
             7    |   GND  | <-> |   GND  |   7