08/15/86
								   8/86
		   Installation and Configuration Information
		    for the 1200 Series Xebec HD Controllers


	   The 1210 controllers are designed for hard disk control. The
       1220 Controllers are designed for both Hard and Floppy disk
       control. Each controller is capable of controlling various drive
       configurations.


       JUMPER CONFIGURATIONS
       ---------------------

       1210 A	1210 B

       I/O			 ROM ADDR

       PIN 1 JUMPERED		 PIN 1 OPEN
	   2 JUMPERED		     2 OPEN
	   3 JUMPERED		     3 JUMPERED
	   4 OPEN		     4 JUMPERED
				     5 OPEN
				     6 JUMPERED
				     7 JUMPERED
				    PD JUMPERED

       -----------------------------------------------------------------

       1210 C

       I/O			 ROM ADDR

       PIN 1 OPEN		 PIN 1 OPEN
	   2 JUMPERED		     2 OPEN
	   3 JUMPERED		     3 JUMPERED
	   4 JUMPERED		     4 JUMPERED
	  PD JUMPERED		     5 OPEN
				     6 JUMPERED
				     7 JUMPERED

       -----------------------------------------------------------------

       1220

       W3		 W4		   W5	 DRIVE "C"

       PIN 1 JUMPERED	 PIN 8 JUMPERED    TYPE 0 - JUMPER 1, 2
	   2 JUMPERED	     7 JUMPERED    TYPE 1 - JUMPER 1
	   3 JUMPERED	     6 JUMPERED    TYPE 2 - JUMPER 2
	   4 OPEN	     5 OPEN	   TYPE 3 - ALL OPEN
			     4 JUMPERED
			     3 JUMPERED
			     2 OPEN	   W5	 DRIVE "D"
			     1 OPEN
					   TYPE 0 - JUMPER 3, 4
					   TYPE 1 - JUMPER 3
					   TYPE 2 - JUMPER 4
					   TYPE 3 - ALL OPEN



							PAGE 2	   6/86

       CABLE INSTALLATION
       ------------------
	   After verifying the proper jumper configurations attach the
       34 PIN command cable and 20 PIN data cable to the controller
       board making sure that the colored rib on the cable is attached
       at pin 1. Then install the controller in an expansion slot.


       LOW LEVEL FORMAT PROCEDURE
       --------------------------
	   The following information was furnished by XEBEC Technical
       Support for Xebec HD Controllers.

	   Booting the system from the A: Drive, load the Debug utility
       from the DOS Supplimental Program Diskette. After typing DEBUG, a
       hyphen will appear as the debug prompt, then follow the procedure
       below.

       A:>Debug  (c/r)
       -i 322	 (c/r)
	  xx		 (status byte returned, please note)
       -i 321	 (c/r)
	  C0		 (status byte returned, please note)
       -o 322 0  (c/r)
       -i 321	 (c/r)
	  CD		 (status byte returned, please note)

       -o 320 04 (c/r)	 Note: 04 is the value for Drive C.
			       substitute 20 if formatting Drive D.
       -o 320 00 (c/r)
       -o 320 00 (c/r)
       -o 320 00 (c/r)

       -o 320 05 (c/r)
       -o 320 07 (c/r)	 Note: change to o320 17 for an embedded
			       servo drive

	   At this point, the drive light should come on indicating
       that the drive is formatting, when the light goes out (after
       3 - 15 minutes depending on disk capacity), continue with the
       following:

       -I 321	 (c/r)
	  CF		 (status byte returned, please note)
       -I 320	 (c/r)
	  00		 (00 indicates that the format command has
			 completed successfully.)

       Note:- if any other value is returned, repeat the procedure.
	      If the condition persists, contact the Xebec distributer
	      for assistance.

       -Q		 (Debug quit command)

	   At this point you should be back at the DOS prompt. Place
       the DOS System Disk in drive A, type in FDISK, set the partition,
       and perform your high level format.